DIVISION 08 - OPENINGS

SECTION 08 71 13 POWER DOOR OPERATORS

Specifier Note: Coordinate and edit articles and paragraphs below to suit project requirements. Add section numbers and titles per CSI "MasterFormat" and specifier's practice. Consult with manufacturer regarding performance requirements for units applicable to project, as well as related equipment and accessories required.

PART I – GENERAL

1.01 SUMMARY

A. 	WORK INCLUDED: Furnish exterior and interior power door operators with housing and visible mounting, as specified, that have been manufactured, fabricated and installed to maintain performance criteria stated by manufacturer without defects, damage or failure. Automatic door operators shall be configured as follows:

1. 	Single doors: Outswing or Inswing.

2.  Simultaneous pairs: Outswing or Inswing.

3. 	Double Egress: Outswing and Inswing.

B. 	RELATED WORK:

1.	Division 8 Section "Aluminum Doors and Frames" for entrances furnished separately.

2.	Division 8 Section "Door Hardware" for hardware to the extent not specified in this Section.

3.	Division 16 Section for electrical connections including conduit and wiring for power door operators.

1.02  REFERENCES

A.	AMERICAN ARCHITECTURAL MANUFACTURERS ASSOCIATION (AAMA):

1. AAMA 101: North American Fenestration Standard/Specification for windows, doors, and skylights.

2. AAMA 611: Voluntary Specification for Anodized Architectural Aluminum.

B. 	AMERICAN ASSOCIATION OF AUTOMATIC DOOR MANUFACTURERS (AAADM).

C. 	AMERICAN NATIONAL STANDARDS INSTITUTE (ANSI):

1. 	ANSI A156.19: For Power Assist and Low Energy Power Operated Doors

2. 	ANSI.117.1: Accessible and Usable Buildings and Facilities

D. 	AMERICAN SOCIETY FOR TESTING AND MATERIALS (ASTM) B221: Aluminum-Alloy Extruded Bars, Rods, Shapes and Tubes.

E. 	AMERICANS WITH Disabilities Act (ADA) 1990

F. 	BUILDING OFFICIALS AND CODE ADMINISTRATORS INTERNATIONAL (BOCA)

G.	INTERNATIONAL CONFERENCE OF BUILDING OFFICIALS / UNIFORM BUILDING CODE (ICBO/UBC)

H.	International Code Council / International Building Code (ICC/IBC)

I. 	NATIONAL FIRE PROTECTION ASSOCIATION (NFPA) 101:

1.	NFPA 70: National Electrical Code (NEC).

2.	NFPA 80: Standard for Fire Doors and Other Opening Protectives.

3.	NFPA 101: Code for Safety to Life from Fire in Buildings & Structures.

J. 	THE ALUMINUM ASSOCIATION (AA) Aluminum Finishes Manual.

K. 	UNDERWRITERS LABORATORY, INC. and CANADIAN STANDARDS ASSOCIATION (USA & CANADA)

1. UL 325: Electrical Door, Drapery, Gate, Louver, and Window Operators and Systems.

2. CSA 22.2-247: Operators and Systems of Doors, Gates, Draperies, and Louvres.

1.03  SUBMITTALS

A. 	PRODUCT DATA: Submit manufacturer's complete product and installation data.

B. 	SHOP DRAWINGS: Submit drawings showing layout, elevations with dimensions, profiles, product components including anchorage, accessories, finish, wiring diagrams, and glazing details (where required).

C. 	CLOSEOUT SUBMITTALS: Submit the following:

1. 	Owner’s Manual.

2. 	Warranty document as specified herein.

3. 	AAADM inspection compliance form completed and signed by certified AAADM inspector prior to doors being placed in operation as proof of compliance with ANSI A156.19.

1.04  QUALITY ASSURANCE AND PERFORMANCE REQUIREMENTS

A. 	INSTALLERS QUALIFICATIONS: Installer shall be factory trained, certified by AAADM, and experienced to perform work of this section.

B. 	MANUFACTURER’S QUALIFICATIONS: Manufacturer to have minimum (10) ten years successful experience in the fabrication of automatic doors of the type required for this project. Manufacturer capable of providing field service representation during installation, approving acceptable installer and approving application method.  Manufacturer shall be a member of AAADM.

C.	CERTIFICATIONS: Automatic sliding door systems and options shall be factory certified to meet performance design criteria in accordance with the following standards:

1.	ADA 1990: Americans With Disabilities Act

2.	ANSI A156.19: Standard for Power Assist and Low Energy Power Operated Swinging Doors

3. 	ANSI.117.1: Accessible and Usable Buildings and Facilities

4.	NFPA 101: Code for Safety to Life from Fire in Buildings & Structures.

5.	UL 325: Electrical Door, Drapery, Gate, Louver, and Window Operators and Systems.

6.  CSA C22.2-247: Operators and Systems of Doors, Gates, Draperies, and Louvres.

7.	BOCA: Means of Egress, Power Operated Doors

8.	ICBO/UBC: Egress Through Lobbies

9.	ICC/IBC: Egress Section

D.	SOURCE LIMITATIONS: Obtain automatic door operators through one source from a single manufacturer.

E.	Product Options:  Drawings indicate sizes, profiles, and dimensions of automatic entrance door assemblies, based on the specific system indicated.  Refer to Division 1 Section "Product Requirements."

F.	Power Operated Door Standard: ANSI/BHMA A156.19.

G. OPERATION: “Knowing Act” and/or Manual:

1. 	“Knowing Act” activation device (Pushbutton/Push plate switch, touchless sensor, etc.) actuates door to open; door closes after time delay expires. Opening and closing force, measured 1" (25.4 mm) from the latch edge of the door, not to exceed 15 pounds (67 N) of force to stop the door when operating in either direction. Operator to include the following variable adjustments so as to comply with ANSI Standard A156.19: Opening time – 4 1/2 to 6 seconds; Closing time – 4 1/2 to 6 seconds.

2. 	Manual: Push-N-Go™: Manually pushing or pulling door activates automatic opening cycle; door closes after time delay expires.

3.  Supported Option: Fire Detection System input with field selectable input to:

a.  Inhibit powered opening (fire door), or

b.  Open and hold open (smoke evacuation door).

H.	Electrical Components, Devices and Accessories:  Listed and labeled as defined in NFPA 70, Article 100, by a testing agency acceptable to authorities having jurisdiction, and marked for intended use.

I.	OPERATING RANGE: -30° F to 130° F (-34° C to 54° C)

J. 	OPENING FORCE REQUIREMENTS FOR Egress doors: In the event power failure to the operator, swinging automatic entrance doors shall open with a manual force, not to exceed 30 lbf (133 N) applied at 1” (25 mm) from the latch edge of the door.

K. 	DOOR ENERGY: The kinetic energy of a door in motion shall not exceed 1.25 lbf-ft (1.69 Nm).

L.	CLOSING TIME:

1. 	Doors shall be field adjusted to close from 90 degrees to 10 degrees in 3 seconds or longer.

2. 	Doors shall be field adjusted to close from 10 degrees to fully closed in not less than 1.5 seconds.

1.05  WARRANTIES

A. 	MANUFACTURER'S WARRANTY: Units to be warranted against defect in material and workmanship for a period of one year from the Date of Substantial Completion.  Manufacturer's warranty is in addition to, and not a limitation of, other rights owner may have under Contract Documents.

B. 	DISTRIBUTOR'S WARRANTY: One year warranty: Labor & transportation charges for defective parts replacement.

1.06  PROJECT CONDITIONS AND COORDINATION

A.	Field Measurements: Verify actual dimensions/openings by field measurements before fabrication and record on shop drawings.

B.	COORDINATION: Coordinate with fabrication and construction schedule to avoid construction delays.

1.	Coordinate with door, door frame, and hardware contractors to insure proper size, hand, and finish.

2.  Coordinate with electrical contractors for power, activate switch, and fire alarm wiring.

1.07 DELIVERY, STORAGE AND HANDLING

A. 	ORDERING AND DELIVERY: Comply with factory's ordering instructions and lead time requirements. Delivery shall be in factory's original, unopened, undamaged containers with identification labels intact.

B. 	STORAGE AND PROTECTION: Provide protection from exposure to harmful weather conditions and vandalism.

PART ll - PRODUCTS

2.01  MANUFACTURER

Horton Automatics, a division of Overhead Door Corporation, shall manufacture automatic swing door operator(s) of type(s) and size(s) specified on plans and door schedule.

2.02  EQUIPMENT

A. 	MANUFACTURED DOOR UNITS: FLEXSWING™: Surface Applied Operator with connecting arms and linkage shall provide positive control of door through entire swing cycle; units shall support use of butt hung, continuous, offset, swing-clear, and center pivot doors.

1. 	Mounting: The operator header shall be mounted to the surface of the existing door frame or wall.

2. 	Door Arms: Connecting hardware shall be a double arm arrangement that can either push the door or pull the door open to suit the job condition. When the operator mounting is on the pull side and a perpendicular wall is within 4" (102 mm) of the door frame, a parallel arm with slide track should be specified.

3. 	Fasteners and Accessories:  Manufacturer's standard corrosion-resistant, non-staining, non-bleeding fasteners and accessories compatible with adjacent materials.

B. 	HEADER CASE: Shall be a side access extruded aluminum case. Standard header size shall be 4" x 5" (102 mm x 127 mm) (height x depth) with extruded ridges full length of header.

C.	OPERATOR: The Electric Operating Mechanism shall be FlexSwing: Operator shall be mounted and concealed in an extruded aluminum case for smooth and quiet operation. Maximum current draw shall not exceed 3.15 amps.

1. 	Opening Action: Shall be accomplished by a D.C. permanent magnet motor working through reduction gears to the output shaft.

2. 	Field Adjustable Spring Closing Action: shall be accomplished by a field replaceable spring. When the door is in the closing mode or fully closed, motor voltage shall not be required and will be off. The door can be manually operated with power on or off, without damage to the operator and will provide controlled closing.

3.  Independent Adjustable Closing and Latching Speed Control: The operator shall employ independent field adjustment of closing and latching speeds.

4.	Field Adjustable Open Stop: The operator shall provide a field adjustable open stop to accommodate opening angles from 80 to 135 degrees without the need for additional components.

5.	Consistent Cycle: The operator shall deliver an even, consistent open force across the entire transition from door fully closed to door open check. Additionally, the range of the force shall be field adjustable to accommodate a wide range of on-site conditions.

6.	Manual Use: Operator to function as manual door closer in direction of swing with or without electrical power.

7.	Controller Protection: The controller shall incorporate the following features to ensure trouble free operation:

a.	Automatic Reset upon power up.

b.	Main fuse and electronic surge protection.

c.	Internal power supply protection.

8.	Soft Start/Stop: The operator shall have field adjustable acceleration and deceleration parameters for smooth normal opening and recycle operation.

9.  Mode Control Switch: Door operators shall be equipped with a three-position function switch to control the operation of the door. Control switch shall provide three modes of operation: Automatic, Off, and Hold-Open.

10.	Door can be used manually, with or without power, without damage to the operator. Without power, operator will allow manual opening with low force required, and will close the door at a controlled slow speed.

11. 	Master Control: Microprocessor-based and shall include a 40-character alphanumeric display to provide ease of adjustment and comprehensive diagnostics, including error and alarm logging. All speed, forces and time delays shall be independently adjustable. External module is not required for adjusting parameters.

a. 	Field adjustable, independent time delays for open cycle, obstruction, and partial open functions.

b. 	Independent adjustment of open speed, open check speed, close speed, close check speed, obstruction speed, acceleration, and deceleration for smooth operation and compliance with applicable standards.

c.	Detection of door motion obstruction in open direction with reducing power opening, and in the close direction with recycling the door back open.

d. 	Motor Protection Circuit: A locked door motor protection circuit will be supplied that will shut off current to the motor when the door is inadvertently locked or otherwise prevented from opening.

e.	Automatic locking: Dry contacts, rated 5 Amp, 250VAC, included to support security door locking with fail safe, fail secure, and momentary locks.  Control software coordinates operator function with lock function.

f.	Sensor Inputs are provided for both activate and safety functions.  Control shall support monitoring of any presence sensors which support this function. (Note: Sensors are not required by ANSI A156.19 Standard for Power Assist and Low Energy Power Operated Swinging Doors.)

2.03  RELATED EQUIPMENT

A.	“KNOWING ACT” ACTIVATING DEVICE: Shall be located on each side of the opening as per ANSI Safety Standard A117 and shall be hardwired to door operator controls.  Activating device shall be momentary contact assembly in one of the following configurations:

1.	PUSHBUTTON: 1" diameter (25 mm) round, red pushbutton switch. Face plates shall be engraved with the international symbol for accessibility and “Press to Open”. Jamb or wall mounted.

2. 	PUSH PLATE: 6" (152 mm) diameter round or 4 ½” (114 mm) square, stainless steel switch. Wall mounted. Optional wireless configuration using radio frequency transmission to receiver located in operator housing.

Optional engravings shall be:

a.	International symbol for accessibility and “Press to Open”.

b.	International symbol for accessibility only.

c.	“Press to Open” only.

d.	Plain - No engraving

3.	TOUCHLESS SENSOR: 1 ¾” (44.5 mm) Jamb-mount, 4 ½” (114 mm) square, or 6” (152 mm) diameter round configurations shall be actuated by waving a hand or solid object in front of sensor surface.

B.	SAFETY DEVICE: Operator shall support non-contact sensors if specified, providing both safety (stop during opening) and recycle (reopen during closing) functions. Operator shall support monitoring of any presence sensors which support this function. (Sensors not required by ANSI A156.19 Standard for Power Assist and Low Energy Power Operated Swinging Doors.)

2.04  RELATED WORK REQUIREMENTS

ELECTRICAL: Provided under Division 16: 120 / 220 VAC, 50/60 Hz, 1 Ø, 15 amp service. Non-North American can be 240 VAC (240 volt power supply to be specified for the operator).

2.05  MATERIALS, FINISHES AND FABRICATION

A. 	EXTRUDED ALUMINUM: ASTM B221, 6063-T5 alloy and temper, anodized: Structural Header Sections: Minimum 1/8" (3 mm) thickness.

B. 	FINISHES (for all exposed aluminum surfaces): Shall be one of the following:

1. 	215-R1 Clear: Arch. Class 1 Clear Anodized Coating, AA-MI2C22A41.

2. 	313-R1 Dark Bronze: Arch. Class 1 Anodized Coating, AA-MI2C22A44.

3. 	312-R1 Light Bronze: Arch. Class 1 Anodized Coating, AA-MI2C22A44.

4. 	315-R1 Black: Arch. Class 1 Anodized Coating, AA-MI2C22A44.

5. 	Special Paint Coating: Color as selected.

6. 	Clad with stainless steel or muntz metal (brass alloy): #7 mirror finish or #4 brushed finish.

PART III - EXECUTION

3.01  EXAMINATION

Site Verification of Conditions: Installer must verify that base conditions previously installed under other sections are acceptable for product installation according to manufacturer's instructions. Notify the Contractor in writing of conditions detrimental to the proper and timely completion of work. Do not start work until all negative conditions are corrected in a manner acceptable to the installer and manufacturer.

3.02  INSTALLATION

A. 	GENERAL: Install equipment per factory’s installation instructions. Installer to be factory trained, certified by AAADM, & experienced to perform work in this section. Install equipment plumb, level & true to line, without warp or rack of frames or sash with factory’s prescribed tolerances. Provide support & anchor securely in place.

B. 	DISSIMILAR MATERIALS: Comply with AAMA 101, Appendix Dissimilar Materials by separating aluminum materials and other corrodible surfaces from sources of corrosion or electrolytic action contact points.

C. 	WEATHER-TIGHT CONSTRUCTION: Install header and framing members in a bed of sealant or with joint filler or gaskets. Coordinate installation with wall flashings and other components of construction.

D. 	ELECTRICAL: General or electrical contractor to install all wiring to operator on a separate circuit breaker routed into header.

E. SIGNAGE: Signage shall be installed, visible on both sides of the door, in compliance with the requirements of ANSI A156.19 Standard for Power Assist and Low Energy Power Operated Swinging Doors.

3.03  CLEANING, ADJUSTMENT AND PROTECTION

A. 	CLEANING: After installation, installer to take following steps:

1. Remove temporary protection of adjacent work areas. Remove construction debris from construction site and legally dispose of debris.

2. Repair or replace damaged installed products. Clean product surfaces and lubricate operating equipment for optimum condition and safety.

B. 	ADJUSTMENT: AAADM certified technician to provide inspection to assure compliance with ANSI A156.19.

C. 	ADVISE CONTRACTOR: Of precautions required through the remainder of the construction period, to ensure that doors will be without damage or deterioration (other than normal weathering) at the time of acceptance.

D.	FIELD QUALITY CONTROL: Testing Services:  Factory Trained Installer shall test and inspect each swinging automatic entrance door to determine compliance of installed systems with applicable ANSI standards.

Note: Horton Automatics reserves the right to make product improvements and change specifications without notice.

END OF SECTION